## Slide 1: VEGAS: A Soft Vector Processor
Aaron Severance
Some slides from Prof. Guy Lemieux and Chris Chou

## Slide 2: Outline
Motivation
Vector Processing Overview
VEGAS Architecture
Example programs
Advanced Features

## Slide 3: Motivation
DE1/DE2 Audio/Video processing options
  NIOS: Easy but slow
  Customize system: Fast but hard
  VEGAS: Pretty fast, pretty easy
VEGAS processor is in v4 build of UBC’s DE1 media computer
  Speed up applications yet still write C code

## Slide 4: Overview of Vector Processing

## Slide 5: Acceleration with Vector Processing
Organize data as long vectors
Data-level parallelism
Vector instruction execution
  Multiple vector lanes (SIMD)
  Repeated SIMD operation over length of vector
Source
vector
registers
Destination
vector
register
Vector lanes
for (i=0; i<NELEM; i++)
a[i] = b[i] * c[i]
vmult a, b, c
Notes: Long vectors of 32 and above
Vector addressing
  Efficient way to gather data
  Eliminates pack/unpack instructions
Will be discussed more on the next slide

## Slide 6: Advantages of Vector Processing
Simple programming model
  Short to long vector data parallelism
  Regular, easy to accelerate
Scalable performance and area
  DE1 only has room for one vector lane, but removing other components could make room for more
  Larger FPGAs can support multiple lanes
    Same exact code runs faster
Notes: Scalable to different maximum vector lengths and numbers of parallel pipelines
Regular, makes it easy to accelerate
Shown by Berkeley VIRAM vector processor project to work better than SS and VLIW in data-parallel embedded workload
Soft vector processor abstracts FPGA resources

## Slide 7: Hybrid vector-SIMD
for( i=0; i<NELEM; i++ ) {
C[i] = A[i] + B[i]
E[i] = C[i] * D[i]
}
0
1
2
3
C
E
C
E
4
5
6
7

## Slide 8: VEGAS Architecture

## Slide 9: VEGAS Architecture
Scalar Core:
NiosII/f @ 200MHz
DMA Engine & External DDR2
Vector Core:
VEGAS @ 120MHz
Concurrent Execution FIFO synchronized
VEGAS

## Slide 10: Key Features of VEGAS
Configurable vector processor
  Selectable performance/area tradeoff
    Working in FPGA: 1 lane … 128 lanes
    More lanes possible
  Fracturable ALUs: 1x32, 2x16, 4x8
  Scratchpad-based “register file”
    Very long vectors
    Explicitly managed memory communication
Notes: Allows area customization according to application requirements
Will discuss customizable aspects in a later slide

## Slide 11: Scratchpad Memory
0
0
1
1
3
3
4
4
5
5
7
7
One vector
(eg, V0)
No vector length restrictions
No address alignment (starting offset) restrictions
Distributed
Vector data
+ AF

## Slide 12: Scratchpad Memory in Action
Vector Scratchpad Memory
Vector Lane 0
Vector Lane 1
Vector Lane 2
Vector Lane 3
srcA
srcB
Dest
srcA
srcB
Dest
Notes: Start with double pumped memory to allow exclusive port for concurrent DMA access, hides memory latency. Then do animation.

## Slide 13: Scratchpad Memory in Action
srcA
Dest

## Slide 14: Performance
Benchmark | NiosII/f | VEGAS |  | NiosII/V32 Speedup
 |  | V1 | V32 | 
fir | 509919 | 85549 | 4693 | 108x
motest | 1668869 | 82515 | 24717 | 67x
median | 1388 | 185 | 7 | 208x
autocor | 124338 | 45027 | 2822 | 44x
conven | 48988 | 3462 | 1897 | 25x
imgblend | 1231172 | 175890 | 35485 | 34x
filt3x3 | 6556592 | 813471 | 75349 | 87x
Notes: Build new table, only only nios, v1, v32, and v32/nios speedup

## Slide 15: Example Problems

## Slide 16: Overall Process
Allocate vectors in scratchpad
Move data from memory  scratchpad
Point vector address registers to data in scratchpad
Perform vector operation
Move data from scratchpad  memory
Check result using Nios

## Slide 17: Example #1: Vector * Constant
int data[128] = { 0, 1, 2, 3, 4, 5, ... , 127 };
int multiplier = 3;
Allocate vectors in scratchpad
int *vector_data;
vector_data = vegas_malloc( 128*4 ); // 128 words long, in scratchpad
Move data from memory  scratchpad
vegas_dma_to_vector( vector_data, data, 128*4 );// copy from ‘data’
Point vector address registers to data in scratchpad
vegas_set( VADDR, V1, vector_data ); // can use V1 .. V7 address reg.
vegas_set( VCTRL, VL, 128 ); // # of elements
Perform vector operation
vegas_wait_for_dma(); // wait for DMA copy to finish
vegas_vsw( VMULLO, V1, V1, multiplier ); // only 1 VEGAS instruction
Move data from scratchpad  memory
vegas_instr_sync(); // wait for all VEGAS instr
vegas_dma_to_host( data, vector_out, 128*4 ); // copy results back
vegas_wait_for_dma(); // wait for DMA copy to finish

## Slide 18: Example #1: Vector * Constant
int data[128] = { 0, 1, 2, 3, 4, 5, ... , 127 };
int multiplier = 3;

## Slide 19: Example #1: Vector * Constant
int data[128] = { 0, 1, 2, 3, 4, 5, ... , 127 };
int multiplier = 3;
Allocate vectors in scratchpad
Move data from memory  scratchpad
Point vector address registers to data in scratchpad
Perform vector operation
Move data from scratchpad  memory

## Slide 20: Example #1: Vector * Constant
int data[128] = { 0, 1, 2, 3, 4, 5, ... , 127 };
int multiplier = 3;
Allocate vectors in scratchpad
int *vector_data;
vector_data = vegas_malloc( 128*4 ); // 128 words long, in scratchpad
Move data from memory  scratchpad
Point vector address registers to data in scratchpad
Perform vector operation
Move data from scratchpad  memory

## Slide 21: Example #1: Vector * Constant
int data[128] = { 0, 1, 2, 3, 4, 5, ... , 127 };
int multiplier = 3;
Allocate vectors in scratchpad
int *vector_data;
vector_data = vegas_malloc( 128*4 ); // 128 words long, in scratchpad
Move data from memory  scratchpad
vegas_dma_to_vector( vector_data, data, 128*4 );// copy from ‘data’
Point vector address registers to data in scratchpad
Perform vector operation
Move data from scratchpad  memory

## Slide 22: Example #1: Vector * Constant
int data[128] = { 0, 1, 2, 3, 4, 5, ... , 127 };
int multiplier = 3;
Allocate vectors in scratchpad
int *vector_data;
vector_data = vegas_malloc( 128*4 ); // 128 words long, in scratchpad
Move data from memory  scratchpad
vegas_dma_to_vector( vector_data, data, 128*4 );// copy from ‘data’
Point vector address registers to data in scratchpad
vegas_set( VADDR, V1, vector_data ); // can use V1 .. V7 address reg.
vegas_set( VCTRL, VL, 128 ); // # of elements
Perform vector operation
Move data from scratchpad  memory

## Slide 23: Example #1: Vector * Constant
int data[128] = { 0, 1, 2, 3, 4, 5, ... , 127 };
int multiplier = 3;
Allocate vectors in scratchpad
int *vector_data;
vector_data = vegas_malloc( 128*4 ); // 128 words long, in scratchpad
Move data from memory  scratchpad
vegas_dma_to_vector( vector_data, data, 128*4 );// copy from ‘data’
Point vector address registers to data in scratchpad
vegas_set( VADDR, V1, vector_data ); // can use V1 .. V7 address reg.
vegas_set( VCTRL, VL, 128 ); // # of elements
Perform vector operation
vegas_wait_for_dma(); // wait for DMA copy to finish
vegas_vsw( VMULLO, V1, V1, multiplier ); // only 1 VEGAS instruction
Move data from scratchpad  memory

## Slide 24: Example #1: Vector * Constant
int data[128] = { 0, 1, 2, 3, 4, 5, ... , 127 };
int multiplier = 3;
Allocate vectors in scratchpad
int *vector_data;
vector_data = vegas_malloc( 128*4 ); // 128 words long, in scratchpad
Move data from memory  scratchpad
vegas_dma_to_vector( vector_data, data, 128*4 );// copy from ‘data’
Point vector address registers to data in scratchpad
vegas_set( VADDR, V1, vector_data ); // can use V1 .. V7 address reg.
vegas_set( VCTRL, VL, 128 ); // # of elements
Perform vector operation
vegas_wait_for_dma(); // wait for DMA copy to finish
vegas_vsw( VMULLO, V1, V1, multiplier ); // only 1 VEGAS instruction
Move data from scratchpad  memory
vegas_instr_sync(); // wait for all VEGAS instr
vegas_dma_to_host( data, vector_out, 128*4 ); // copy results back
vegas_wait_for_dma(); // wait for DMA copy to finish

## Slide 25: Example: Brighten Screen
RGB packed into 16-bits (5-6-5)
for(y = 0; y < MAX_Y_PIXELS; y++){
pPixel = getPixelAddr(0,y);
for(x = 0; x < MAX_X_PIXELS; x++){
colour = *pPixel;
r = (colour >> 10) & 0x3E;
g = (colour >> 5) & 0x3F;
b = (colour << 1) & 0x3E;
r = min(r+2,62);
g = min(g+2,63);
b = min(b+2,62);
colour = (r<<10) | (g<<5) | (b>>1);
*pPixel++ = colour;
}
}

## Slide 26: Designing for VEGAS
Brighten one row of pixels at a time
Move row into scratchpad
Process data
  Separate into R, G, and B vectors
  Add 2 to each
  Check for overflow
Move data back to main memory
See vegas_demo1.c in hw files on website

## Slide 27: Setting up vectors/address registers
Pointers point to vectors in scratchpad
unsigned short *vR;
unsigned short *vG;
unsigned short *vB;
Malloc allocates space for the vector
vR = vegas_malloc(MAX_X_PIXELS*sizeof(unsigned short));
vG = vegas_malloc(MAX_X_PIXELS*sizeof(unsigned short));
vB = vegas_malloc(MAX_X_PIXELS*sizeof(unsigned short));
Address registers get set to pointers
vegas_set(VCTRL,VL,MAX_X_PIXELS);
vegas_set(VADDR,V1,vR);
vegas_set(VADDR,V2,vG);
vegas_set(VADDR,V3,vB);

## Slide 28: Transferring data to the scratchpad
for(y = 0; y < MAX_Y_PIXELS; y++){
DMA transfer line to scratchpad
pLine = getPixelAddr(0,y);
vegas_dma_to_vector(vR, pLine, MAX_X_PIXELS*sizeof(unsigned short));
Wait until finished before processing
vegas_wait_for_dma();

## Slide 29: Process data (part 1)
Data in R. Separate R,G,B
vegas_svh(VSLL,V3,1,V1); //b = line << 1;
vegas_svh(VSRL,V2,5,V1); //g = line >> 5;
vegas_svh(VSRL,V1,10,V1); //r = line >> 10;
vegas_vsh(VAND,V3,V3,0x3E); //b = b & 0x3E;
vegas_vsh(VAND,V2,V2,0x3F); //g = g & 0x3F;
vegas_vsh(VAND,V1,V1,0x3E); //r = r & 0x3E;
svh means ‘scalar-vector halfword’
  vs means ‘vector-scalar’, vv ‘vector-vector’
  h=halfword, b=byte, w=word
VSLL/VSRL are opcodes
  Some have an unsigned variant ending in U
Destination, Source A, Source B

## Slide 30: Process data (part 2)
Add two and check for overflow
vegas_vsh(VADD,V3,V3,2); //b = b + 2;
vegas_vsh(VADD,V2,V2,2); //g = g + 2;
vegas_vsh(VADD,V1,V1,2); //r = r + 2;
vegas_vsh(VMIN,V3,V3,62); //b = min(b,62);
vegas_vsh(VMIN,V2,V2,63); //g = min(g,63);
vegas_vsh(VMIN,V1,V1,62); //r = min(r,62);
Merge back into packed RGB form
vegas_svh(VSRL,V3,1,V3); //b = b >> 1
vegas_svh(VSLL,V2,5,V2); //g = g << 5
vegas_svh(VSLL,V1,10,V1); //r = r << 10
vegas_vvh(VOR,V3,V3,V2); //b = b | g
vegas_vvh(VOR,V3,V3,V1); //b = b | r

## Slide 31: Transfer back to main memory
Wait for vector core to finish
vegas_instr_sync();
Merge back into packed RGB form
vegas_dma_to_host(pLine, vB, MAX_X_PIXELS*sizeof(unsigned short));
Don’t have to wait_for_dma() until you read data

## Slide 32: Advanced: Double buffering
Example starts DMA, immediately waits
  But vector core and DMA can be concurrent
Use two buffers
  Transfer to one while processing the other
  Switch buffers when done
See vegas_demo2.c for an example

## Slide 33: More advanced Features
Data-dependent conditional execution
  Vector flag registers
Vector addressing modes
  Unit stride
  Type conversion
  Constant stride
Source
registers
Destination
register
Flag
register
Vector Merge Operation

## Slide 34: Example: Simple 5x5 Median Filtering
Pseudocode (Bubble sort)
Load the 25 pixel vectors P[0..24]
For i=0 to 12 {
minimum = P[i]
For j=i+1 to 24 {
if (P[j] < minimum) {
  swap (minimum, P[j])
  }
  }
}
Slide “window” after 1 median
  Each window 5x5 values
  Each value = CPU register
Repeated over entire image
  1st Window = Vector[0]
  2nd Window = Vector[1]
  VL = # of windows
Output pixel
Output pixel
Notes: Minimum is a vector
Base address and stride registers

## Slide 35: Example: Simple 5x5 Median Filtering
Bubble sort on vector registers
Vmin,Vmax to do swap
“VL” results at once!
25 rows ->
25 vector registers
“VL” pixels each